## Slide 1: Side-Channel and Fault Attack Lab

## Slide 2: Lab Session
Outline:
  Timing attack: Password Checker
  SPA: RSA Square & Multiply
  Fault Attack: RSA Bellcore Attack
  Fault Attack: Password Checker Emulator

## Slide 3: Lab Session
Outline:
  Timing attack: Password Checker
  SPA: RSA Square & Multiply
  Fault Attack: RSA Bellcore Attack
  Fault Attack: Password Checker Emulator

## Slide 4: Timing Attack
✓
✓
✕
✓
✓
✓
✓
✕
✓
✓
✓
✓
✕
✓
✓
✓
✓
✕
✕
✕
With Timing Oracle
Constant Time Oracle
In naïve scenario, the comparison is done one at a time resulting in timing leakage

## Slide 5: Lab Session
Outline:
  Timing attack: Password Checker
  SPA: RSA Square & Multiply
  Fault Attack: RSA Bellcore Attack
  Fault Attack: Password Checker Emulator

## Slide 6: Simple Power/EM Analysis (SPA/SEMA)
Adversary learns secret information by visual inspection of (usually single) power/EM measurement
Ex: observe square & multiply in exponentiation etc.
Common Targets:
  Key dependent operations, number of rounds/operations, memory access pattern, etc
Source: https://anysilicon.com/side-channel-attacks-differential-power-analysis-dpa-simple-power-analysis-spa-works/
1
2
3
4
5
6
Key Recovery from RSA Exponentiation
No. of Function Calls

## Slide 7: Square & Multiply
An efficient way of computing Cd mod n is using an algorithm called square-and-multiply
Let's compute 117^65 mod 133
Convert 65 to binary  0b1000001
We started with C=117
  Bit 0=1: 117
  Bit 1=0: 117^2 mod 133 =123  S
  Bit 2= 0: 123^2 mod 133 = 100  S
  Bit 3= 0: 100^2 mod 133 = 25  S
  Bit 4= 0: 25^2 mod 133 = 93  S
  Bit 5= 0: 93^2 mod 133 = 4  S
  Bit 6= 1: (4^2 * 117) mod 133 = 10  SM

## Slide 8: SPA on RSA: Square & Multiply
SPA Leakage
Protection
Ciphertext C, Modulus n, R=1
for i from k-1 to 0 do
R= R^2 mod n
if i=1 then
R= R*C mod n
Return R
Ciphertext C, Modulus n, R=1
for i from k-1 to 0 do
R0= R^2 mod n
R1= R*C mod n
R= Ri
Return R
0b011011010000

## Slide 9: Find the Key
1 0 1 1 0 1 1 0 = 0xB6

## Slide 10: Lab Session
Outline:
  Timing attack: Password Checker
  SPA: RSA Square & Multiply
  Fault Attack: RSA Bellcore Attack
  Fault Attack: Password Checker Emulator

## Slide 11: RSA Fault Attack: Bellcore
Factor modulus by introducing errors in exponentiation and CRT (Chinese Remainder Theorem)
Signature
  , or
  , or
Attack: corrupt only one of the two exponentiations

## Slide 12: RSA Attack: Bellcore
Attack: corrupt only one of the two exponentiations
Assume is corrupted by fault injection:
Compute
Observe shares the factor with
Compute , q=N/p
Notes: \cite{http://euler.ecs.umass.edu/research/bbkn-IEEEP-2012.pdf}

## Slide 13: Lab Session
Outline:
  Timing attack: Password Checker
  SPA: RSA Square & Multiply
  Fault Attack: RSA Bellcore Attack
  Fault Attack: Password Checker Emulator

## Slide 14: How Compiler Works
Basic illustration on how computer processes high level programming language

## Slide 15: Bypass Password Check (Fault)
Task:
Given the binary for a basic password check. Gain a successful password check by skipping a specific instruction
Task:
Given the binary for a basic password check. Gain a successful password by introducing a “Delayed” Fault